## Slide 1: RE1/1 Additional Services
Chamber RE+1/1/1 - 4
The services are all there as planned;
HV, LV, Cooling and Gas.
Since the change to use the Link system in the towers we require;
Signal and DCS
Ian Crotty 7 August 2014

## Slide 2: Routing as supplied by Integration
16 Signal Cables dia 10mm
4 DCS cables dia 5mm
2 paths to reduce cable section over CSCs
Choice of Rack access from bottom or top

## Slide 3: ME1/2 & 1/3
Access is not possible to the base of the rack X4J32 as the floor slot is insufficient
Cables go over both the ME1/2 & 1/3. Going under 1/3 is not easy for this quantity. 2m slack will be stored under the green structure so chambers can be removed.
Removal of the floor above racks is necessary

## Slide 4: ME1/1
RE1/1/01
RE1/1/04
Thin red line represents the cable path

## Slide 5: Modified routing
The 2 white DCS cables go beside the present very full cables paths
Obstruction of the ME1/1s is limited.
These cables can be readily disconnected at the RE1/1 end to allow full access for ME1/1 chamber removal.
This is not so true for the Signal cables as the connectors are fragile.
DCS cables already connected

## Slide 6
Cables (DCS) show the route along side the alignment system, behind the N2 seal bracket and over the ME1/2
Alignment protection
Old CSC cables do not give a problem

## Slide 7: Cables for RE1/1/01 & 02
X8 Signal cables laid in place.
X2 DCS cables laid in place.
This work was carried out with
Victor Perelygine and verified by Alexandre Kurenkov

## Slide 8: Remaining questions
Attaching the cables (x8) on to the ME1/2 & ME1/3s.
Will the alignment system (black box) remain in the ME1/1 nose area ?
If the alignment system stays then the cables can go lower down on the next slot.

## Slide 9: Photos

## Slide 10: Space if alignment not present