## Slide 1
Signal Processing

## Slide 2: PM Operation
Philips XP2041 5” dia cathode 14 dynodes + focussing electrodes
Socket FE1120 pin connections
Sockets
PA
a
c
PM schematic
U(t)
t
Fast PM: pulse rise time ~2ns, gain: 3.107
PM Voltage divider (progressive) U0=2000V
PM
Sc
mu-metal shield tube provides protection from external B field.
mu metal soft iron

## Slide 3: Pre-Amplifiers
Amplify weak detector signals (mV)  1V, transmit through cable. Main types: charge-sensitive or voltage-sensitive
Charge sensitive preamps integrate directly Q(t)  Edeposit For semiconductor IC diodes (small signals). Voltage sensitive preamps amplify U(t) = Q(t)/C, C = const.!  PM, PC
Detector: capacitor Cd,  charge Q(t), current I=dQ/dt
For E measurement, integrate Q
For t measurement, differentiate Q
Use operational amplifiers (op-amp) for both.
+
-
U0
R
R,C
Q
Cd
Cd
R
C
Replacement circuit for detector and decoupling

## Slide 4: Basic Counting System
Detector
Ground
Bias (U0)
R
C
-+ - - +-+ +- -+++
Pulse Height Analysis 
Digitization
R: Load resistor C: Insulate electronics from HV (det. Bias) Pulse height ~100 mV
Charge sensitive preamplifier: Voltage output pulse height (1V) independent of detector C
Amplifier/Shaper: differentiates (1x or 2x)
Final amplitude 2-10V
Binary data to computer
PreAmp
Amp
Shaper
unipolar
bipolar
0
DU
t
t
DAQ

## Slide 5: Operational Amplifier Principle
G
+
-
Op Amp inputs: Inverting (-), non-inverting(+)
Integrated Circuit Chip (IC) 411 Op Amp

## Slide 6: Operational Amplifiers
Inverting amplifier (gain G~106). Properties of amp determined by feedback:
Feed back negative of input signal to the summation point cancels the signal at S,
Integrator
G
+
-
Uin
- 106 · Uin
Rf
G
+
-
Rin
S
G
+
-
Rin
S
Cf
G
+
-
Cin
S
Rf
Differentiator
Iin
If

## Slide 7: Comparator/Digitizer
Functionality:
0≤ Uout ≤ +5V
Initially (Uin open, not connected) + input at UThr =+2.5 V
If Uin < +2.5 V  R3 no current
 Uout = 5V
If Uin > +2.5 V  R3 max current
 Uout = 0V
Device essentially digitizes analog pulse amplitude.
Stack of several  ADC
>
+
-
R1
R2
R3
2.5 V
5 V
0 V
t
U

## Slide 8: Charge Sensitive Preamp
Inverting, integrating preamp
Pulse decay governed by tdec1/RfCf.
Additional amplifier necessary for pulse shaping and gain.
G
Cf
Rf
Cd
Rin
U
t
S

## Slide 9: Main/Shaping Amplifiers
Tasks: 1) Linear amplification to pulse heights of U (1-10)V 2) Improvement of signal/noise ratio (integration) 3) Pulse shaping (Gaussian shape is best)
Cd1
Rd1
RI
CI
Cd2
Rd2
1st diff integr 2nd diff
More versatility: RC-circuits  active filters

## Slide 10: NIM Signal Standards
(National Instruments Methods)
Linear analog NIM signals
+10V
0V
“1”
“0”
+10V
0V
“1”
+5V
“0”
0V
TTL-Logic
Slow logical NIM (TTL) pulses:discriminators, gates,…
-16mA -0.8V/50W
2ns
Fast logical NIM signals for fast timing/triggering
NIM-gate/trigger signal

## Slide 11: Discriminator/Trigger
R1
Rf
Mono Vibrator
+10V
Udisc
Input
Output
Task: Produce a logical signal, whenever analog signal exceeds threshold Udisc. Use for logical decisions (open acquisition,...). Exists for slow and fast pulses.
For fast timing, use negative NIM logic units
Udisc
Uin
t
t
Uout
-
+
S
Potentiometer

## Slide 12: Zero-Crossing Triggering
t
Produce fast, bipolar linear pulse. Possible: different gains for positive and negative parts  zero crossing at different times (fraction of time to maximum)
Produce “saturated” uniform pulse
Differentiate saturated pulse, use triplet pulse as input for trigger (negative pulse polarity).
Trigger output appears at zero crossing
(Internal delays here neglected)
t
t
Utrig
Trigger output signal
t

## Slide 13: Constant-Fraction Discriminator
Uin
-1
Delay Td
S
Uf=f·Uin
Trigger
Zero crossing timing (@ fraction f of amplitude): always at same physical t independent of amplitude (fixed pulse shape): No “walk” with energy
Ucftd
Amplitude dependent leading edge discr. output timing
Can utilize for PSD!
t pulse time jitter
“walk”
Udisc
Splitter
E pulse amplitude spectrum

## Slide 14: Logic Modules
U1
U2
Uout=U1LU2
Overlap Coincidence
U2
U1
Or (inclusive)
U1
U2
Uout
t
t
t
U1
U2
Uout
t
t
t
Uout=U1VU2
Anti-Coincidence/Veto
U
U
complement
U1
U2
Uout= U1LU2
U2
For fast timing: use fast negative logic

## Slide 15: Signal Transmission
inner conductor
outer conductor/shield
outer conductor
dielectric medium
outer casing
Coaxial cables/transmission lines  traveling waves in cavity resonators
Wave equation (R=0):
z
L: inductivity/length C: capacity/length depend on diameter and dielectric
signal propagation speed (speed of light):
typically c-1=5 ns/m
characteristic resistance Z0=Ohmic resistance! For R≠0, Z0(w) complex
Z0 = 50 W or 93 W used for timing, spectroscopy, resp.

## Slide 16: Impedance Matching
Rd
Rload
Rd
Rload
sender
receiver
For impedance matching, Rload=Z0, cable looks infinitely long: no reflections from end.
For mismatch, Rload ≠ Z0, reflection at end, traveling back, superimpose on signal  terminate with Rterm.
Polarity of reflected signal Rload=0, ∞
Rterm

## Slide 17: Cable Reflections
Receiver input impedance Rload ≠ Z0,  use additional Ohmic termination in parallel
Rload
Rterm
L
L
Open end: Rload= ∞ Input and reflection equal polarity, overlap for t > 2Tcable
Tcable = 2L/c
Short: Rload=0, Input and reflection opposite polarity, superposition = bipolar
Multiple (n) reflections attenuated by R-n

## Slide 18
The End