## Slide 1: Leaks on RE4s Feb 2016
Ian Crotty
21 March 2016

## Slide 2: Information already available or to be produced
1 Leak on RE+4/3/22
2 Leaks on RE+4/2/06
1 leak on RE-4/X/27
Tersts in 904 QC4
The “Tightness” of all unions on RE+4 (“tightness” = swag level)
Unions produce by ZEC
Unions produced by Sagana tooling
Tigtness versus leak rate

## Slide 3: Leak Rates RE+4 after repairs on 22 and 6
SS Ferruled chambers
“Acceptable leak Rate” (ALR) = 5E-2 [mBar.l/s]
The leak rate appears higher at 12 than at 18 Bar
Chart: Sector [60deg]
| 21-26 | 15-20 | 27-32 | 02-33 | 09-14 | 03-08
RE+4 @ 12 Bar | 0.021042 | 0.22444 | 0.048095 | 0.035439 | 0.17908 | 0.039608
RE+4 @ 18Bar | 0.056111 | 0.019804 | 0.028056 | 0.025897 | 0.11222 | 0.012024
Sector 9-14 has factor 3-4 higher than “ALR”.
However the ALR does not give the Volume
Sector 15-20 passes @ 18Bar
There appears no correlation with SS ferrules

## Slide 4: “Tightness”, the level at which the union has been tightened.
Bulkhead
Union
Locknut is always inside the chamber
Thread pitch is 20 tpi = 1.254mm

## Slide 5: Schematic of SM cooling System
Type 2 Out Low R
Type 2 In Low R
Type 2 In High R
Type 3 Out Low R
Type 3 In Low R
Type 3 Out High R
Type 3 In High R
Type 2 Out High R
There are 2 ends to each union, one inside and the other outside
“R”
Inside
Outside
Histograms will be made for all 8 positions to look for differences between SS and Brass ferruled unions.

## Slide 6: Specified “tightness” or swag
Before Tightening 4.83mm
After Tightening 3.62mm
Instructions in French
Pitch is 20tpi (1.254mm). 1 ¼ turns = 1.568mm. But the Difference in Shim is 4.83-3.62 = 1.21mm which is 0.96 turns.
The question is the point at which the 1 ¼ turns is started. The shim tool necessitates tools to achieve the “Serrage a la main” !

## Slide 7
Chart: Outer Union "Tightness"
| 1.8 | 1.9 | 2 | 2.1 | 2.2000000000000002 | 2.2999999999999998 | 2.4 | 2.5 | 2.6 | 2.7 | 2.8 | 2.9 | 3 | 3.1 | 3.2 | 3.3 | 3.4 | 3.5 | 3.6 | 3.7 | 3.8 | 3.9 | 4 | 4.0999999999999996
T2OutsmallR | 0 | 1 | 2 | 0 | 0 | 2 | 3 | 3 | 2 | 9 | 9 | 4 | 15 | 17 | 11 | 16 | 53 | 34 | 29 | 5 | 1 | 0 | 0 | 0
T2OutHighR | 0 | 0 | 0 | 0 | 1 | 7 | 5 | 8 | 16 | 17 | 19 | 28 | 28 | 29 | 21 | 21 | 6 | 5 | 3 | 0 | 1 | 1 | 0 | 0
T3OutsmallR | 0 | 0 | 0 | 1 | 4 | 5 | 3 | 0 | 9 | 11 | 23 | 25 | 26 | 25 | 32 | 16 | 14 | 17 | 3 | 1 | 0 | 1 | 0 | 0
T3OutHighR | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 3 | 1 | 3 | 14 | 15 | 15 | 23 | 13 | 23 | 30 | 19 | 30 | 15 | 4 | 4 | 2 | 1

## Slide 8
Chart: Type 3 Out High R
| 1.8 | 1.9 | 2 | 2.1 | 2.2000000000000002 | 2.2999999999999998 | 2.4 | 2.5 | 2.6 | 2.7 | 2.8 | 2.9 | 3 | 3.1 | 3.2 | 3.3 | 3.4 | 3.5 | 3.6 | 3.7 | 3.8 | 3.9 | 4 | 4.0999999999999996
Brass Ferrules | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 2 | 13 | 11 | 13 | 16 | 6 | 13 | 22 | 8 | 22 | 14 | 1 | 2 | 0 | 0
SS Ferrules | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 3 | 1 | 1 | 1 | 4 | 2 | 7 | 7 | 10 | 8 | 11 | 8 | 1 | 3 | 2 | 2 | 1
Looking at the level of swaging for each of the 8 positions across the radius.
3.23 | 3.29
0.31 | 0.35
Brass Ferrules
SS Ferrules
Mean
StDev
Tighter
1 ¼ turns = 3.4 ± 0.1[mm]

## Slide 9
Chart: Type 3 Out Low R
| 1.8 | 1.9 | 2 | 2.1 | 2.2000000000000002 | 2.2999999999999998 | 2.4 | 2.5 | 2.6 | 2.7 | 2.8 | 2.9 | 3 | 3.1 | 3.2 | 3.3 | 3.4 | 3.5 | 3.6 | 3.7 | 3.8 | 3.9 | 4 | 4.0999999999999996
SS ferrules | 0 | 0 | 0 | 0 | 1 | 2 | 1 | 0 | 1 | 5 | 6 | 11 | 4 | 12 | 12 | 4 | 2 | 9 | 0 | 1 | 0 | 1 | 0 | 0
Brass Ferrules | 0 | 0 | 0 | 1 | 3 | 3 | 2 | 0 | 8 | 6 | 17 | 14 | 22 | 13 | 20 | 12 | 12 | 8 | 3 | 0 | 0 | 0 | 0 | 0
Tighter
1 ¼ turns = 3.4 ± 0.1[mm]
Brass Ferrules
SS Ferrules
Mean
StDev
3.19 3.02
0.36 0.32
4 Unions over tight, perhaps to reduce leak rate in QC4

## Slide 10
Chart: Type 3 In High R
| 12.2 | 12.3 | 12.4 | 12.5 | 12.6 | 12.7 | 12.8 | 12.9 | 13 | 13.1 | 13.2 | 13.3 | 13.4 | 13.5 | 13.6 | 13.7 | 13.8 | 13.9 | 14 | 14.1 | 14.2 | 14.3 | 14.4 | 14.5 | 14.6 | 14.7
SS ferrules | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 3 | 0 | 5 | 8 | 7 | 4 | 9 | 11 | 9 | 7 | 5 | 4 | 0 | 0 | 0 | 0 | 0 | 0
Brass Ferrules | 0 | 1 | 1 | 0 | 3 | 7 | 1 | 1 | 3 | 1 | 3 | 5 | 10 | 5 | 9 | 12 | 16 | 21 | 14 | 12 | 7 | 2 | 6 | 2 | 1 | 1
An example of the inner (lock nut end) of the union “tightness”
13.57 | 13.66
0.28 | 0.48
Brass Ferrules
SS Ferrules
Mean
StDev
13.66 13.57
0.48 0.28

## Slide 11: Conclusions
From the leak tests done there appears no correlation between SS ferrules and leaks.
This may be due to the closeness of the mean SS and mean Brass values.
The spread seen in the histograms is large
Tightening of the unions not yet understood but ongoing.
Request ZEC to make up 10 unions and measure
Sagana shim tool are not correct (!!) for the unions supplied.
We HAVE to improve our assembly technique
Further Work
Complete histograms for all positions in radius.
Make measurements of leak rate vs “tightness”
Understand leak rate vs Test pressure.
Should we improve the leak test procedure
Introduce yearly leak tests and inspections.

## Slide 12: Additional Material
Sagana Catalogue
http://www.rotarex.191.it/Collegamenti/Sagana%20-%20Raccordi%20a%20compressione%20doppia%20ogiva%20.pdf
From the Oxford dictionary
The term "swage" comes from the Old French term souage, meaning "decorative groove" or "ornamental moulding".
Notice the name of the company “Swagelok”