## Slide 1: Updates on RPC RE3/1 and RE4/1
1,2 E. Voevodina, 3 I. Crotty, 2,3 S. Buontempo,
3B. Smiljkovic
1 Universita Federico II di Napoli, 1-80125 Napoli,
2 Istituto Nazionale di Fisica Nucleare (INFN), Sezione di Napoli,
3 European Organization for Nuclear Research, Geneva (Switzerland)
RPC Upgrade Workshop, 14-15 March 2017

## Slide 2: Plan
1. RE3/1:
Studies of the value “Z” for RE3/1 (four methods of the determining) ;
Fastening elements for fixing RE3/1 chambers on the YE3.
2. RE4/1:
Studies of the value “Z” for RE4/1;
Mounting plates for RE4/1 chambers ;
The proposed MP outer “R” M24 posts which are underneath the RE4 SMs.
3. Future work for RE3/1 and RE4/1
Conclusion
RPC Upgrade Workshop, 14-15 March 2017 02/19

## Slide 3: Four methods to determine the value "Z" for RE3/1
Main drawing of the CMS;
Manual measurements;
Laser scanner and laser tracker;
IR - sensors.
RPC Upgrade Workshop, 14-15 March 2017 03/19

## Slide 4
The value "Z" for RE3/1
1. Main drawing
On basis the main drawing of the CMS the value "Z" for RE3/1 is 88 mm!
RPC Upgrade Workshop, 14-15 March 2017 04/19

## Slide 5
The value "Z" for RE3/1 from manual measurements is 80 mm! IO requires more 20 mm for clearance between CSC and RPC.
* The features design of the CSC chamber were taken into account.
* Manual measurements in P5 was 19 of December 2016
Principle scheme for determination the value “Z ”
2. Manual measurements
The value "Z" for RE3/1
(650+19)-523-66 = 80 mm
- 523 mm is CSC thickness
- 66 mm is the neutron shielding
RPC Upgrade Workshop, 14-15 March 2017 05/19

## Slide 6
The value "Z" for RE3/1
3. Laser scanner and laser tracker
* Laser scanning in P5 was done 19 of December 2016 (for YE-2 and YE-3 around the ME-3/1/13) and 10 of January 2017 (for YE+2 and YE+3 around the ME+3/1/13)
ME+3/1/13
Neutron shielding
RE +3/2
YE/+2
YE/+3
Height Collar is 19. 6 mm
Height Collar is 648. 6 mm
RPC Upgrade Workshop, 14-15 March 2017 06/19

## Slide 7
RPC TC working meeting 7/
The value "Z" for RE3/1
Main results from laser scanner :
Surfaces between YE-2 / / YE+2 and YE-3// +3 around the CSC chambers ME/-3/1/13 // ME/+3/1/13 (below the beam pipe on far side ) have been measured;
The topology of CSC chambers is determined very good;
The average error of the best-fit is :
for YE/-2 and YE/-3 is +/-1.8 mm;
for YE/+2 and YE/+3 is +/-3.0 mm.
The maximum error is :
for YE/-2 and YE/-3 is +/-2.5 mm;
for YE/+ 2and YE/+3 is +/-3.0 mm.
The height of the collars are:
for YE/+3 is 19.6 mm; for YE/-3 is 20.4 mm;
for YE/+ 2 is 648.6 mm; for YE/- 2 red disk not measured.
These values agree with the manual measurements.
The position of five M12 holes measured in the area of YE/+3 in front of the
CSC chamber ME+3/1/13.
Inspection of the positions of the M12 holes
RPC Upgrade Workshop, 14-15 March 2017 07/19

## Slide 8
The value "Z" for RE3/1
4. IR sensors
* IR sensors were installed in 10th of January 2017
Results will be come later after closing YE/+2 and YE/+3.
RPC Upgrade Workshop, 14-15 March 2017 08/19

## Slide 9
Conclusion
Table of the main results
Main parameters | CMS drawing | Manual measurements | Laser scanner | IR sensors
1. Distance between YE2 and YE3 , mm | 655 | 650 + 19 = 669 | 648.6 + 19.6 = 668.2 | ­-
2. Thickness of the neutron shielding, mm | 63 | 64.5 ÷ 66.0 |  | -
3. Distance between YE2 and max. higher surface of the CSC chamber, mm | 524 | 523 |  | -
4. Available space for RE3/1, mm | 88 | 80 ± 0.5 | 79.5 ± 3.0 | Data will come soon
RPC Upgrade Workshop, 14-15 March 2017 09/19

## Slide 10
Fastening elements for mounting RE3/1 chambers on the YE3
M12 mounting holes
1
2
3
4
5
6
Each RE3/1 chamber is fixed at six points
1. Mounting of the RE 3/1 chambers on the YE3
RPC Upgrade Workshop, 14-15 March 2017 10/19

## Slide 11
2. Mounting brackets for the RE 3/1 chambers
1
2
3
4
4
3
1, 2 and 3
Slot
Ф 12.5
Ф 12.5
Ф16
Ф16
Ф16
Slot
1, 2
M12
Fastening elements for fixing RE3/1 chambers on the YE3
The stiffeners
Degrees of freedom are not fully defined
RPC Upgrade Workshop, 14-15 March 2017 11/19

## Slide 12
Supplementary inner “R” mounts RE3/1 chambers on the YE3
3. Mounting arcs for the RE 3/1 chambers
Brackets
Arc Plate for inner “R” of RE3/1
Mounting Arc Plate on the neutron shielding
Screw with countersunk head
At the present time the cylindrical screws heads protrude beyond the shield.
Arc Plate for inner “R” are hidden under the RE3/1
RPC Upgrade Workshop, 14-15 March 2017 12/19

## Slide 13
Mock up for RE3/1
Work schedule
RPC Upgrade Workshop, 14-15 March 2017 13/19

## Slide 14
Studies of the value “Z” for RE4/1
Available space for RE4/1 chambers
On basis the main drawing of the CMS the value "Z" for RE4/1 is 85 mm.
At the present the IO thinks that there is only 80 mm available.
During the RE4/2 Super Module assembly the extra space was available and so the distance between CSC and RPC was increased.
The space between neutron shielding and RE4/1 should be a minimum of 20 mm;
Thickness of the RE4/1 “on” yoke is 25 mm;
Thickness of the RE4/1 “off” yoke is 25 mm;
The value gap is 5 mm;
Thickness Alu mounting plates is 8 mm.
___________________________
Total: 83 mm
Thus, we have the available space for RE4/1 chambers
without overlap!
Assembly RE4/1 chambers without overlap
Once this design we will be able to study the overlap configuration.
RPC Upgrade Workshop, 14-15 March 2017 14/19

## Slide 15
Mounting plate for RE4/1 chambers
Mounting plates
RPC Upgrade Workshop, 14-15 March 2017 15/19
Thickness is 8 mm
Preliminary design of the mounting plate

## Slide 16
The proposed MP outer “R” M24 posts which are underneath the RE4 SMs
Two interesting questions:
How to mount the frame using the mounting positions M24?
How to attach the RE4/1 chambers on the frames?
Principle scheme
Mounting posts M24
Or another version
Area of mounting
M24
Screw
Flange
RPC Upgrade Workshop, 14-15 March 2017 16/19

## Slide 17
Conclusion
RE3/1:
On the basis all received results we have the value “Z” for RE3/1 chambers 80 mm;
The RE3/1 chambers brackets and mounting plates for fixing were drawn;
Next step will be study of the Patch Panel and connectors with cables outside the chamber.
RE4/1:
The available space for RE4/1 chambers is about 80 mm. It isn’t enough for RE4/1 chambers with overlap (total space for RE4/1 chamber with overlap is 83mm);
RE4/1 FEBs are visible and accessible in this design.
RPC Upgrade Workshop, 14-15 March 2017 17/19

## Slide 18
Future work for RE3/1 and RE4/1
1. Section for RE3/1:
Neutron shielding support will require modification;
IR sensors will give definitive “Z” value;
Full photographic record for ME3/1 (cabling, pipes and etc.)
Mock up for PP and services over 60 degree in 904;
“B” field deflection of YE3 and YE2 should be negligible but to be checked .
2. Section for RE4/1
Require ME4/1 laser scan
Install MP in P5 to study CSC services;
Install IR sensors in RE4/1 gap for real “Z” values;
Measure YE4 deflection with IR sensors;
Mock up of MP and chambers in 904.
RPC Upgrade Workshop, 14-15 March 2017 18/19

## Slide 19
Thanks for attentions!

## Slide 20
Backup

## Slide 21: Scan
Scan YE/-2

## Slide 22
Scan YE/-3

## Slide 23
RE3/1
RE4/1
RE4/1
Design of the RE3/1 and RE41 chambers
Thicknesses RE3/1 and RE4/1 are 25 mm.

## Slide 24
Available space for mounting FEBs
Available space for mounting FEBs is 68 mm
Distance between YE3 and RE3/1 chamber “on” yoke is 68 mm
Cross section YE3
Space between RE3/2 and RE3/1 for the cooling/power connectors