## Slide 1: LV cable production
Ian
11 Feb 2019

## Slide 2
Use the LV Link board cable, used for the initial installation
2 x 2.5mm2 (13AWG) + 2 x 0.22mm2 (24AWG )
Sheath diameter = 8.3mm approx. (8.22mm)
Perhaps we have 3.5km available
P5 was not able to measure this !

## Slide 3
Connecteur cote Chambre
Thermo retractable , protection Etiquettes

## Slide 4
Thermo retractable , Raychem 12/4-0-STK
Tresse poly et Cuivre
Tresse Cu04.01.33.050.5
Nominal dia. 6mm
Sheath dia. 4 -7mm
160 wires of 15/100

## Slide 5
8.3mm
Thread dia.
3.38mm
6-32 UNC inch thread
https://www.caen.it/products/a3009b/
https://www.boltdepot.com/fastener-information/machine-screws/machine-screw-diameter.aspx

## Slide 6
Lug dia 6mm
Section 2.5mm2
https://www.cabac.com.au/brands/cabac/lugs-links-and-terminals/lugs-and-links/copper-crimp-lugs/cu-crimp-15-95mm2/10100505?s=
T90-25mm 90 Degree Angle Battery End Termi
Ring terminal,

## Slide 7
https://www.domcar.com.au/p/2-5mm2-copper-lug-m4/

## Slide 8
Lusin input week 2
https://www.klauke.com/en/electrical/electrical-connection-systems/
Gustav Klauke GmbH Auf dem Knapp 46 42855 Remscheid Deutschland Tel.: +49 (0)2191 / 907-0 Fax: +49 (0)2191 / 907-141 E-Mail: Klauke-Info@Emerson.com

## Slide 9
PS end
Lugs and Sense wire connectors
Sense wire connectors 232-9959 (RS)
Pins 233-0038 (RS) or Farnell 182206-2

## Slide 10
Pins
Farnell
Power
2433225 female
2433223 male
Sense
http://www.farnell.com/datasheets/1836823.pdf?_ga=2.199927789.278703743.1546866397-246438842.1465995239
http://www.farnell.com/datasheets/1836824.pdf?_ga=2.199927789.278703743.1546866397-246438842.1465995239

## Slide 11
Hood is therefore for a 15pin size connector
447-7353
Drawing
https://docs-emea.rs-online.com/webdocs/167c/0900766b8167c5a2.pdf
09.21.23.013.7 Straight outlet cover high section 8,5 mm FMK21G 2
OR
For dia 12,5 mm cable FMK2G SCEM 09.21.23.013.9
For dia 9,6 mm cable with 45deg entry FMK21 09.21.23.022.0 4.1chf

## Slide 12
https://www.norcomp.net/series/962-series

## Slide 13
Grounding of the cable shield.
Two solutions ;
By ground cable to star point on the chamber patch panel. Is the shield isolated from the body or both body and flying lead ground wire are used (ground strap).
By the screws in the body. The shield has to be screwed to some where in the body.
The shield consists of the braid and the nude cable

## Slide 14
The 45 deg connector housing is very difficult to mount with cable bending radius and stress make it unlikely., to be seen with manufacturer.
45 Degree cable exit
Cable is not straight into the pin next to the screw on the inner radius

## Slide 15
Questions of pin layout.
Pin gender mixed , female on cable ?
Positive on for the RHS of the PS.
Put positive on the rhs of the connector as seen from the back of the connector in order to be intuitive.
The above also true for the sense wires
3 spare wires in the connector, can they be used ?

## Slide 16
From Christoph 5 Feb 2019
Insulated PP made from PCB
10Euro for >75 pieces

## Slide 17: Conclusion from 904 installations. Cable has female pins and cable body is male

## Slide 18
Lengths by S. Bally from the IO
X4 Far
X2 Near

## Slide 20
Draft lengths done. Slack to be added

## Slide 21: Visit to the production site at Boudry 5 Feb 2019

## Slide 22: Conclusions
Material can be provided by Cavitech, cost increase on Cavitech contract.
We will arrange quantities and component supply in order to remain below the 5kchf
They will produce 36 cables rapidly. Request 160.
The PS lug they will source.
I must provide final details of flexible lengths for quote.
Exact pin-out details arranged during visit.

## Slide 23
Pin-out decided at Cavitech according the accepted norms.