## Slide 1
OF Installation
Andres with input from numerous colleagues
11 Feb 2019

## Slide 2
USC Rack
February 11th, 2019
2
3.1 and 4.1 station fiber system components
YE3
YE1
Patch Panel 1
Patch
Panel 2
Mini Cable Chain
Main Cable Chain
Patch Panel 3
UXC
USC
Cable 2
Cable 3
RPC Backend
FEB
RE+4/1
Cable 1
Cable 4
To be installed 72 Chambers in total.
18 chambers -> RE+3/1 (72 fibers) 18 chambers -> RE-3/1 (72 fibers)
18 chambers -> RE+4/1 (72 fibers) 18 chambers -> RE-4/1 (72 fibers)
FEB
RE+3/1
2 fibres from each FEB
2 FEB per chamber
4 fibres per chamber
Not including spares
Assuming standard 144 fiber cable
(gives 72 fibers used + 72 spares) ->1 cable per station
Two panels: Positive and negative side
One panel

## Slide 3
February 11th, 2019
3
Supply Summary and Lead Time
CERN Reference | Description | Length (m) | Quantity | Section | Name in these slides
RPC_C1 | LC-LC simplex patch cord | 37 | 576 | 3.3.1 | Cable 1
RPC_C2 | 144-fiber cable: 144 LC to 6xMTP24(F) | 30 | 4 | 3.3.2 | Cable 2
RPC_C3 | 144-fiber cable: 144 LC to 6xMTP24(M) | 65 | 4 | 3.3.2 | Cable 3
RPC_C4 | 12-fiber cable: 12 LC to MTP12(F) | 2 | 30 | 3.3.3 | Cable 4
RPC_PP1 | Customized patch panel | n/a | 4 | 3.3.4 | Patch Pannel 1, Patch Pannel 3
RPC_AA1 | Adapter array | n/a | 2 | 3.3.5 | Patch Panel 2
RPC_BOX1 | Box to protect adapter array | n/a | 2 | 3.3.6 | Patch Panel 2
Supplies | Lead time
RPC_C1, RPC_C2 (25%) | 4 weeks
RPC_C1, RPC_C2 (75%) | 8 weeks
RPC_C3, RPC_C4, RPC_PP1, RPC_AA1, RPC_BOX1 | 12 weeks

## Slide 4
February 11th, 2019
4
OM3 vs OM4 prices
SYLEX |  | PRICES IN: | USD |  |  |  | 
Table 3: RPC |  |  |  |  |  |  | 
 | Description | Quantity | Unit Price OM4 | Total price OM4 | OM3 decrease (per unit) | Total price OM3 | Difference total price OM4 and OM3
1 | RPC_C1 | 576 | 22.08 | 12718.08 | 2.55 | 11249.28 | 1468.8
2 | RPC_C2 | 4 | 1462.49 | 5849.96 | 288.9 | 4694.36 | 1155.6
3 | RPC_C3 | 4 | 2367.45 | 9469.8 | 625.95 | 6966 | 2503.8
4 | RPC_C4 | 30 | 65.99 | 1979.7 | 1.34 | 1939.5 | 40.2
5 | RPC_PP1 | 4 | 976.75 | 3907 | 0 | 3907 | 
6 | RPC_AA1 | 2 | 88.34 | 176.68 | 0 | 176.68 | 
7 | RPC_BOX1 | 2 | 36.4 | 72.8 | 0 | 72.8 | 
TOTAL PRICE RPC FOR TENDER FORM: |  |  |  | 34174.02 |  | 29005.62 | 5168.4
FIBERNET |  |  |  |  |  |  | 
Table 3: RPC |  |  |  |  |  |  | 
 | Description | Quantity | Unit Price OM4 | Total price OM4 | OM3 decrease (per unit) | Total price OM3 | Difference total price OM4 and OM3
1 | RPC_C1 | 576 | 19.8 | 11404.8 | 3.7 | 9273.6 | 2131.2
2 | RPC_C2 | 4 | 2154 | 8616 | 420 | 6936 | 1680
3 | RPC_C3 | 4 | 3210 | 12840 | 910 | 9200 | 3640
4 | RPC_C4 | 30 | 58.95 | 1768.5 | 2.6 | 1690.5 | 78
5 | RPC_PP1 | 4 | 560 | 2240 | 0.0 | 2240 | 
6 | RPC_AA1 | 2 | 73 | 146 | 0.0 | 146 | 
7 | RPC_BOX1 | 2 | 187 | 374 | 0.0 | 374 | 
TOTAL PRICE RPC FOR TENDER FORM: |  |  |  | 37389.3 |  | 29860.1 | 7529.2

## Slide 5
February 11th, 2019
5
Remarks
The color of the cables is magenta (the standard for OM4 cables).
Sylex is proposing also duplex LC connectors for cable 1 (instead of simplex). Both options are available.
LC Simplex
LC Duplex
Proposed “patch panel 1” is made of Aluminium
Proposed material for the “patch pannel 2”
is plastic PC/ABS.

## Slide 6
UXC Inspection or routing 6 Feb 2019
YE3 PP 5 possible locations
On top of X5 racks as CSC
Under the floor or on top

## Slide 7
YE1 PP possible locations
Fibre routing up to mCC is not obvious

## Slide 8
Near +Z MCC is very full !
Near –Z has ample space

## Slide 9
RB present FO PP

## Slide 11
Conclusion
Call for Tender is close to be ready
We have to go back and look at the details of the lengths and the positions of the PP 1 (on YE3)and 2 (On YE 1 PP)
Meeting with S. Bally this Wednesday.