## Slide 1: RE2/2 geometry
979 mm
684 mm
1687 mm
Active area
Layer | Thickness (mm)
Aluminum FEB Cover | 1.8
PCB FEBs FR4 | 1.6
Cu. Cooling panels | 1.15
Aluminum Faraday cage for FEBs | NONE!
Cu. Cooling Pipe (with H2O) | 8
Aluminum Cross Bar | 5
Mylar | 0.3
Copper | 0.1
Mylar | 0.3
Mylar | 0.3
Top hpl out (HV) | 2
Gas Gap | 2
Top hpl in (0V) | 2
Mylar | 0.3
Mylar | 0.3
Cu strips | 0.017
FR4 | 0.4
Mylar | 0.3
Mylar | 0.3
bottom hpl in (0V) | 2
Gas Gap | 2
bottom hpl out (HV) | 2
Mylar | 0.3
Mylar | 0.3
Copper | 0.1
Mylar | 0.3
Aluminum bottom panel | 6
HPL (d = 1.4) composition in mass ratio:
H: 5.74%
C: 77.46%
O: 16.80%
Continuous layers
Gas mixture:
95.4% C2H2F4
4.5% iC4H10
0.3% SF6
95.2%

## Slide 2: RE1/1 geometry
271 mm
453 mm
1007 mm
Active area
Layer | Thickness (mm)
Aluminum FEB Cover | 0.5
PCB FEBs FR4 | 1.6
Cu. Cooling panels | 2
Aluminum Faraday cage for FEBs | 1
Cu. Cooling Pipe dia. (with H2O) | 6
Aluminum Cross Bar | 5
Mylar electrical insulation | 0.2
Total mylar on HV side | 0.4
Copper GND | 0.038
top hpl out | 2
gas gap | 2
top hpl in | 2
Total mylar on GND side | 0.2
Cu strips | 0.017
FR4 | 0.400
Total mylar on GND side | 0.2
bottom hpl in | 2
gas gap | 2
bottom hpl out | 2
Copper GND | 0.038
Total mylar on HV side | 0.4
Mylar electrical insulation | 0.2
Aluminum bottom panel | 5
HPL (d = 1.4) composition in mass ratio:
H: 5.74%
C: 77.46%
O: 16.80%
Continuous layers
Gas mixture:
95.4% C2H2F4
4.5% iC4H10
0.3% SF6
95.2%