## Slide 1
Weld if possible
@155

## Slide 2
Replace with valve OD10
Reduction OD10 OD6
Weld for OD10
OD10 to buffer 20 liters
@155

## Slide 3
Weld one end of flexible OD10-OD10
Weld 150 cm pipe OD10
Weld pipe for pressure sensor connection
Pressure sensor 0-5 barg
@155

## Slide 4
Weld small piece of pipe OD 10 L-shape
Long enough to allow to use connector
@155

## Slide 5
Fix pneumatic valve to rail on the wall
@CMS

## Slide 6
Global view
Bring drill to fix
Compressor
Protection for exctraction pipe
Protection for pipe from compressor to wall to drum and pneumatic
@CMS

## Slide 7
From compressor
Add pressure reducer (Andrea). Then flexible (from drum to filter)
Pipe OD10 from compressor
It can be on the floor (in the corner)
filter
Output drum should be OD12
@CMS
@CMS

## Slide 8
Filter better in vertical
Connection on filter on the contrary of what is written on the filter:
1 is drum side
2 is mixer side

## Slide 9
Pipe from drum
@CMS

## Slide 10
Input of recuperated R134a in mixer
@CMS