## Slide 1: RE3/1 and RE4/1 Integration
Ian Crotty
01 September 2016

## Slide 2: Steps for both RE3/1 & RE4/1
Envelope agreed with Integration Office
Detailed schematic of nominal chamber exterior ( PP and Electronic covers)
Detail design of 1 or 2 chamber technologies
Model (wood or Alu case) of RE3/1 & RE4/1 for installation in P5. Dates ??
Mounting design for RE4/1, complicated concept
Mounting for RE3/1 with present locations or new.

## Slide 3: Envelope
Establish 3D model outer limits, namely touching neighbouring elements , CSCs etc.
Cut back in order to provide agreed clearances wrt neighbours.
Evolve basic chamber
Measure the distances with CMS closed with B= 1 & 0. Basically confirm the 14mm between yokes.

## Slide 4: Installation model for P5
Make at P5 WS a wooden or light weight (10kg) case for verifying P5 envelope, mounting and installation scenarios.
Modify detailed schematic using input from above, there will be detailed changes.

## Slide 5: Detailed schematic
Integrate the basic chamber to the surroundings
  Mounting schematic for both RE3 & 4
  Cooling and gas up to external periphery ( Obtain input form CMS cooling & gas
  Cable paths to rack space.
  This is a big job
  Followed by detailed prototype

## Slide 6: Chamber design for the different designs
If time permits
With collaboration of external institutes come up with a design . This is an iterative process as space is vied for ….. And

## Slide 7: Design or different chambers technology
Obtain basic layout info from China, Lyon, Korea and XX
Propose basic internal design, for all 3 if time permits, to verify validity of these basic assumptions on layout HV and Gas

## Slide 8: Mounting design for RE4/1
The inner radius is simple as the inner CSC mounts are there and available.
The outer radius is more sophisticated as the mounting post is behind the RE4 SM.
There are basically 2 options
either assemble a platform on which the chambers can be mounted.
OR
mount directly to the mounting posts.

## Slide 9: Mounting design for RE3/1
The present mounting points (M12 threaded holes) are for the low Eta coverage..
These points (x4) could be used for a chamber going to high eta.
The question will be to mount “over” the shielding.
The access to the FE should be with no chamber removal.
CSC alignment system use has to be understood.

## Slide 10: Time line
To be discussed with Isabel.

## Slide 11: Conclusion
There is a lot of work to be completed.
Integration of the two stations is quite different.
The sooner we can converge on a technology the easier will be the design work.
Collaboration with IO started well, has slowed over the summer.
Man power, time line ?