## Slide 1: Distance Measurement between CMS Yokes
Ian Crotty
29 Nov 2016

## Slide 2: Use remote sensing IR
Arduino Uno
10 bit ADC
IR Sensor
Measured distance

## Slide 3: Signal from IR sensor
Ambiguous values @ small distances < 2cm

## Slide 4: First results on the Bench (desk)
Chart: Corrected Distance vs Bin No.
| 48 | 72 | 98 | 122 | 130 | 166 | 182 | 186 | 240 | 302 | 402 | 406 | 468 | 495 | 510
Bin No. Vs Distance [mm] | 233 | 170 | 130 | 102 | 76 | 71 | 68 | 54 | 42 | 31 | 25 | 20 | 22
Chart: Inverse Bin Number vs Distance
| 2.0833333333333332E-2 | 1.3888888888888888E-2 | 1.020408163265306E-2 | 8.1967213114754103E-3 | 7.6923076923076927E-3 | 6.024096385542169E-3 | 5.4945054945054949E-3 | 5.3763440860215058E-3 | 4.1666666666666666E-3 | 3.3112582781456954E-3 | 2.4875621890547263E-3 | 2.4630541871921183E-3 | 2.136752136752137E-3 | 2.0202020202020202E-3 | 1.9607843137254902E-3
Uncorrected Data | 233 | 170 | 130 | 103 | 102 | 76 | 71 | 68 | 54 | 42 | 31 | 15 | 18 | 20 | 22
Corrected data | 233 | 170 | 130 | 102 | 76 | 71 | 68 | 54 | 42 | 31 | 25 | 20 | 22

## Slide 5: Conclusion
Seems to give good results in the 30-150mm as announced.
Lower values will have to be sorted due to the response of the IR sensor.
Calibration to be worked on.
Code needs developing for multiple sensors.
Hardware to be made CMS cavern robust.