## Slide 1: Main results received during the EYETS16 for the RE3/1 and RE4/1 envelope
Elena Voevodina, Ian Crotty, Salvatore Buontempo
30/05/2017

## Slide 2
YE3
ME3/1
YE2
RE 3/1
FEB
Neutron shield.
96 mm (IO)
between ME3/1 (HEB) and N. Shield
670 mm
between YE2 and YE3
FEB cover up to PP
HEB
140 mm
between ME3/1 (PCB) and N. Shield
FEB in high R
FEB
Cross section X

## Slide 3
FEB in high R
Length of RPC RE3/1 chamber of 1560 mm

## Slide 4
FEB
FEB
RE3/1
“on”
RE3/1
“off”
Neutron Shield.
Length of 1025 mm
FEB in lower R

## Slide 5: Design RE3/1 and RE4/1 RPC chambers
Cross section of double gap RPC chamber
Double gap RPC chamber
thickness RPC chamber is 25 mm;

## Slide 6: Available value “Z” space for RE4/1 RPC chambers
Name of methods to determine the value “Z" | Distance between YE/ 4 and YE/3, mm | Thickness ME4/1 package, mm | Thickness neutron shielding, mm | Distance between YE/ 4 and ME4, mm
Main drawing of the CMS (3D model) | 655 | 504 | 66 | 151
Available value “Z” will be about (655-504-66) = 85 ± 1 mm
BUT
85 ± 1 mm is not enough space for RE4/1 RPC chambers with overlapping!
Because (85 ± 1) – ( 20 + 25+ 5 +25 + 8) = 3 ± 1 mm,
where
The space between ME4/1 and RE4/1 should be a minimum of 20 mm;
Thicknesses of the RE4/1 “on” yoke and “off” yoke is 25 mm;
The value gap is 5 mm;
Thickness Alu mounting plates is 8 mm.
Thus, we have the available space for RE4/1 chambers without overlapping!

## Slide 7
655 mm
YE3
YE4
RE 4/1
ME4/1
Neutron shield. 66 mm
504 mm
Cross section YE3 and YE4
20 mm
Clearance between ME4/1 and RE4/1