## Slide 1: Capillary tube Δ P measurements
Nicola Lacalamita, Aleksandar Aleksandrov, Roberto Guida
TC meeting,
14/01/2019, CERN, Meyrin

## Slide 2: Experimental setup for ΔP tests
Gas: freon
Rotameter and flowmeter
Pressure sensor
The goal: define the tube specification for RE4.1, RE3.1 impedance boxes.
Two types of capillary:
  OD 1.59mm, ID 0.99 mm (used for RE4)
  OD 1.59 mm, ID 0.87 mm

## Slide 3: Results (1)
Chart: L / h
| 1 | 2 | 4 | 6 | 8 | 10
D99 L120 | 0.35 | 0.53 | 0.95 | 1.44 | 1.93 | 2.58
D99 L100 | 0.33 | 0.48 | 0.87 | 1.3 | 1.79 | 2.38
D99 L80 | 0.3 | 0.41 | 0.7 | 1.04 | 1.42 | 1.9
D99 L60 | 0.28 | 0.36 | 0.64 | 0.95 | 1.3 | 1.74
D99 L40 | 0.25 | 0.31 | 0.51 | 0.75 | 1.04 | 1.4
D87 L120 | 0.43 | 0.69 | 1.39 | 2.11 | 2.89 | 3.86
D87 L100 | 0.41 | 0.62 | 1.17 | 1.77 | 2.45 | 3.28
D87 L80 | 0.35 | 0.56 | 1.02 | 1.54 | 2.18 | 2.87
D87 L60 | 0.34 | 0.5 | 0.89 | 1.34 | 1.87 | 2.51
D87 L40 | 0.3 | 0.38 | 0.7 | 1.07 | 1.49 | 2
D87 L120 bend | 0.48 | 0.84 | 1.82 | 3.07 | 4.47 | 6.14
1 vol/h = 2 l/h

## Slide 4: Results (2)
Chart: Delta P
| 1 | 2 | 4 | 6 | 8 | 10
D87 L120 | 0.43 | 0.69 | 1.39 | 2.11 | 2.89 | 3.86
D87 L100 | 0.41 | 0.62 | 1.17 | 1.77 | 2.45 | 3.28
D87 L80 | 0.35 | 0.56 | 1.02 | 1.54 | 2.18 | 2.87
D87 L60 | 0.34 | 0.5 | 0.89 | 1.34 | 1.87 | 2.51
D87 L40 | 0.3 | 0.38 | 0.7 | 1.07 | 1.49 | 2
D87 L120 bend | 0.48 | 0.84 | 1.82 | 3.07 | 4.47 | 6.14
1 vol/h = 2 l/h

## Slide 5: Results (3)
1 vol/h = 2 l/h
Chart: L / h
| 4 | 6 | 8
D87 L120 | 1.39 | 2.11 | 2.89
D87 L100 | 1.17 | 1.77 | 2.45
D87 L120 bend | 1.82 | 3.07 | 4.47

## Slide 6: Notes and conclusions
The specifications of the capillary tubes is suggested to be:
OD 1.59 mm, ID 0.87 mm, length = 120 mm
To check the ID of the pipes we used drills: 1.0 mm, 0.9 mm and 0.85 mm. For the tube ID 0.87 mm the 0.85 mm drill has to be used.
The swagelok union was tightened according to the specifications or ¾ turn.
It is very important to clean the tube after cutting because it can produce additional delta P (up to 0.5 mbar).
The delta P from 6mm tube may have additional impedance variation in the range [0.2 mbar: 0.5mbar] for pipes with lengths between 6 m and 14 m, measured for flow of 3 vol/h.
In order to decrease the impact of this systematic a new gas layout is proposed: moving from 1 channel =120 ° sector (only TOP/BOTTOM gaps from 6 chambers are connected) to 1 channel = 60 ° sector (both gaps of 3 chambers are connected).

## Slide 7: Gas distribution schematic (1 gas channel = 120° sector)
Bulkhead Swagelok brass union 8 mm
Legris brass unions (6mm)
8 mm copper pipe
6 mm copper pipe
RE4(3).3 chamber
RE4(3).2 chamber
RE4(3).1 chamber
Impedance box
Gas Rack
Top layer
Supply
Return
Parallel flow

## Slide 8: Gas distribution schematic (1 gas channel = 60° sector)
Bulkhead Swagelok brass union 8 mm
Top layer
8 mm copper pipe
6 mm copper pipe
RE4(3).3 chamber
RE4(3).2 chamber
RE4(3).1 chamber
Impedance box
Gas Rack
Bottom layer
Supply
Return
Parallel flow