## Slide 1: HV testing
Ian
Input from S. Lusin
6 April 2019

## Slide 2
Free charge, on the metal surfaces, Surface charge
and bound charge within the dielectric, Volume charge density leaks onto the surface
The latter goes to the former by induction ?
Dielectric absorbtion or “Soakage”.
These two aspects are not the capacitive charge that is removed “instantaneously”

## Slide 3
The test method
A box that ensures that the environmental conditions remain the same.
The cable is tested with no resistance, so that the current drawn does not hide the current taken by the cable itself.
We did not discuss charge up current due to capacitance and polarisation, interesting, length etc
A 10Mohm to bring the cable back to 0 Volt and then quickly to the short in the box then put the clip on to ensure that no charge leaks back to the surface and so avoiding a shock.
The box must be metallic and grouded so avoiding static build up. This is the case with the PS in a “float” configuration.

## Slide 4
The charge(Vol) will “come back” after the test, to the surface, and so must be “equalised “ by maintaining a contact between the inner conductor and the outer one.
Solutions; use a shorted out connector at one or both ends
Or. Devise some form of a clip that is cheaper BUT must remain in place for years until the chambers and/or PS are connected.