## Slide 1: CERN LHC CMS RPC Upgrade
Andrés Cabrera
Ian Crotty
5 Nov 2018

## Slide 2
YE3
YE1
Panel iRPC
Patch
Panel
Mini Cable Chain
Main Cable Chain
Patch Panel
USC
USC Rack
iRPC
UXC
USC
iRPC: 4 fibers per chamber
Number of Chambers:
18 RE+3/1 -> 72 fibers
18 RE+4/1 -> 72 fibers
18 RE-3/1 -> 72 fibers
18 RE-4/1 -> 72 fibers
Trunk Cable 1
Trunk Cable 2
Proposal:
4 Trunk cable 1 (96 fibers: 72 used + 24 spares)
4 Trunk cable 2 (96 fibers: 72 used + 24 spares)
*1 cable per 18 chambers
0.35 dB
0.35 dB
0.35 dB
0.35 dB
0.35 dB

## Slide 3
MTP/MPO connector
24 fibers per connector
Trunk cable option
12 fibers per connector
Male
Male
Female
Female

## Slide 4
Specification Trunk Cable 1 (96 fibers)
Specification Trunk Cable 2 (96 fibers)
Panel iRPC
Patch
Panel
Patch
Panel
Patch Panel
USC
4 MPT/MPO Connectors Female
3 used + 1 spare
(24 fiber per connector)
8 MPT/MPO Connectors Female
6 used + 2 spares
(12 fiber per connector)
4 MPT/MPO Connectors Male
3 used + 1 spare
(24 fiber per connector)
4 MPT/MPO Connectors Male
3 used + 1 spare
(24 fiber per connector)
Length B: 80 m.?
Length A: 1 m. ?
Length : 1 m. ?
Length B: 30 m.?
Length A: 1 m. ?
Length C: 1 m.?

## Slide 5: General Cable Requirements
96 fibers per cable
Multimode OM3
Jacket: Low Smoke Zero Halogen (LSZH)
Compliance with CERN IS23:
https://edms.cern.ch/document/335745/LAST_RELEASED/

## Slide 6: To solve?
Is there enough space for the installation in the main cable chain?
The connectors spread out 10 cm each…
How the connectors are protected when are delivered?
Are protected the connectors to pass the tunnel?